ACE Weekly Report : 9/09/99

Spacecraft Activities:

- All spacecraft subsystems are performing nominally.

Maneuver Activities

The next attitude maneuver is scheduled for 9/9/99.

Instrument Activities

- 9/6/99 - SWEPAM weekly calibrations performed successfully.

- 9/8/99 - Executed OCR SEP-054 to adjust the SEPICA 2kc voltage - Fan 3 pressure had climbed to 12-13 Torr and needed adjustment - OCR classified as routine

Anomalies

- 9/1/99 - Telemetry was interupted between 16:05:24 and 16:22:48 due to loss of both pipes (telemetry transmission lines at 2 different bandwidths) at DSN. See anomaly report #G99-0053 and DR #N51727

- 9/2/99 - Telemetry was lost from 14:48:50 to 15:55:45 due to a SFG failure. See anomaly report #G99-0054 and DR #N51734. It was necessary to recover slices 318-364 and 444-451 on the next dayÕs support, i.e. day 246.

- 9/3/99 - At Precal segment, station did not receive test blocks. Could not establish SFG connection. See anomaly report #G99-0055  and DR #N51753.  Problem cleared up before BOT.

- 9/6/99 - MOC received degraded data throughtout entire support from DSS 66 resulting in approx 260 VC2 frame drops.  Various troubleshooting with D66 and Ops chief did not clear problem.  CDR playback obtained to retrieve data for cleaner data. Due to various frame drops Bin dumps not performed at end of day activity. G99-0056 - Frame Seqeunce Errors  (DR L03594)  Consult Pass plan for Troubleshooting efforts (pg 10).  Full set of SSR data retrieved from a combination of CDR and redump of slices on the following day.

- 9/7/99 - Experienced frequent VC2 frame drops for second time in week using station D66.  Contacted JPL Ops chief to report problem.  JPL comm is presently looking into data problem.  Successfully redumped all relative slices from SSR A.

General

- Held review of Escalation Procedure with Mission Director.  The FOT will further update the escalation procedure and submit to Mission Director for approval.