ACE Weekly Report : 10/5/99

Spacecraft Activities:

All spacecraft subsystems are performing nominally.

Maneuver Activities

Successfully completed stationkeeping maneuver with a spin maneuver on 10/4/99. Successfully completed an attitude maneuver on 10/5/99. The next attitude maneuver is scheduled for 10/12/99 .

Ground System Activities

- 9/30/99 - Successfully simulated a Y2K maneuver with TASS for February 29, 2000.

Instrument Activities

- 9/30/99 - Executed two OCR's for SEPICA 30 kv ramp up -  Continued with OCR SEP-020 pt II for continuation of 30 kv ramp up after 30 kv voltage was reset during previous weekend.  Executed OCR SEP-061 to set 2kc setpoint to H'65' and clear 30 kv discharge flag.

- 10/1/99 - Executed two OCR’s for SEPICA instrument.  OCR SEP-056 was used to adjust F3 2kc setpoint.  OCR-020 used to complete 30 kv ramp up.

- 10/2/99 - Executed OCR SEP-062  Instrumentor continues to adjust Fan 3 2kc setpoint for changes in pressure of Fan 3.  These adjustments are necessary to correctly tune Fan 3 for valid science collection.

- 10/5/99 - Executed OCR SIS-013, SIS_VSTRING - SIS instrument command state change for Helium event enhancement.

Anomalies

- 10/5/99 - ISIS fanout-3 hung, a reboot cleared the problem - twelve min. of recovered data. Anomaly Report # G99-0060