ACE Weekly Report: 03/02/2000

All ACE spacecraft subsystems are performing nominally. A successful attitude maneuver was performed on 2/28/00. The next attitude maneuvers are scheduled for 03/08/00 and 03/17/00. A station-keeping maneuver is scheduled for 03/09/00.

CDR replays do not work. The problem has a fix and will be implemented in release 5.1. For more information, see IDR CDSID # 00015909.

On 2/24/00:

- Observed Sepica Alarm (SSSALARMS =7) indicating a 30 kv discharge. Telemetry check of SSS30KV and verification by instrumenter indicated flag was set by a 30kv current transient. Executed OCR SEP-071 to clear flag

- RTSW observations indicated increase in Solar Wind activity. Executed OCR SEP-072 to temporarily change the gain of the Sepica instruments SSD low gain pixels to improve measurments of energetic He+

On 2/25/00:

- DSN 26 meter automation test was supported during nominal ACE support. Test proved inconclusive and further testing necessary for 26 meter automation and ACE operations compatibility.

- 26-m test support :

- DSS 16 briefed to contact S/C 3-way

- DSS 16 briefed to disable output of telemetry until MOC direction for forward output

- Nominal Support- output data from DSS 66 was disabled and placed in record mode when D16 attempted forwarding data

- Nominal SSR playback data interrupted for approx. 15 minutes and replay of missing data successfully retrieved later during support.

- After several unsuccessful attempts to receive D16 data the test was terminated and D66 data acquired for remainder of support. All activities other than 26 -m auto test were nominal